## Slide 1: Sun Smart project
Group 24
Stella stiven, Bethany kaye-blake, Neil alombro

## Slide 2: Design Context
Skin cancer is the most common form of cancer in New Zealand (~80%)
Resultant health care costs amount to almost $200 million each year, and is only expected to grow
Our UV levels are higher, so we must be proactive to protect our skin
Notes: What you're trying to achieve (including the likely market, and any key requirements and specifications)
How your overall design is structured and how it works (it helps here to refer to schematics and other diagrams)
  What are the major pieces of your design, and what do they do?
  How do the pieces connect together?
  How do all of the pieces work together to do what your design is supposed to achieve?
What your rationale was for key decisions
What evidence you have that the design works as intended
  Results of analysis or simulation that shows how the design satisfies specifications
  A demonstration of your prototype hardware and software

## Slide 3: Design aim
What are we trying to achieve?
A portable device that will inform the user of the UV index and alert them when they should be reapplying sunblock or finding shade based off this UV index.
Our device aims to be an opportunity for awareness, as well as a protective measure when in use
Likely market:
Beach goers, people swimming in outside pools, summer sports/spectators, sunbathers
Notes: What you're trying to achieve (including the likely market, and any key requirements and specifications)
How your overall design is structured and how it works (it helps here to refer to schematics and other diagrams)
  What are the major pieces of your design, and what do they do?
  How do the pieces connect together?
  How do all of the pieces work together to do what your design is supposed to achieve?
What your rationale was for key decisions
What evidence you have that the design works as intended
  Results of analysis or simulation that shows how the design satisfies specifications
  A demonstration of your prototype hardware and software

## Slide 4: Key Requirements
3 main requirements
To educate users about UV Index in New Zealand
To alert users when outside to reapply sun block, or find shade
To utilise the energy from the sun when outside

## Slide 5: Key specifications
Arduino can interpret data from UV sensor and change components to appropriate states such as:
  Tell RGB LED to light up in the correct colour
  Tell the 7-seg what number to display (when button is press AND transducer is OFF)
  Tell the transducer when to buzz (and turn off when button is pressed)
Solar panel needs to provide enough power to the Arduino on a sunny day (5V and 250mA)
  Solar panel is rated 5.5V and 270mA average
Notes: ADD MORE IF YOU THINK OF ANY!!!!

## Slide 6: Overall design
Power Source: Solar Cell
Shield Design
Stand
Arduino
Notes: What your rationale was for key decisions
What evidence you have that the design works as intended
  Results of analysis or simulation that shows how the design satisfies specifications
  A demonstration of your prototype hardware and software

## Slide 7: How it works
UV sensor reads wavelength of UV radiation
Arduino records the measurement from the UV sensor every 60 seconds
Arduino calculates the average UV index
  The calculation bases the indicator on 100 UV index points based on research.
Transducer buzzes when it is recommended to reapply more sunscreen for the UV index
  When transducer is ON: Button pushed = transducer turns off
  When transducer is OFF: Button pushed = UV index number on display turns on
LED is always on and lit up in the UV index colour
This colour will update every 60 seconds when Arduino records the measurement from the UV sensor
Notes: What your rationale was for key decisions
What evidence you have that the design works as intended
  Results of analysis or simulation that shows how the design satisfies specifications
  A demonstration of your prototype hardware and software

## Slide 8: Design: shield design
Main Components
Appropriate access to components
Consistent Power supply
Arduino UNO Microcontroller
(Electronic Data Recorder)
UV Sensor
Transducer
Solar Panel
Button
7 Segment Display
1.5W Power
Digital Data
Digital Data
1.5W Power
RGB LED
Measurement
Digital Data
Digital Data
Notes: Main Components:
Power
Measurements: UV Detector
Information: RGB LED & 7 Segment Display
Alert: Transducer
Component access:
Button
Readability of 7 seg
Attachability of solar cell

## Slide 10: Design: compact stand

## Slide 11: Design: compact stand

## Slide 12: Design structure: software
Modular software design allowed for individual component testing then debugging with overall robot system.
Using Arduino code to combine all components to operate together.
total_uv >= 100
button_state = HIGH
INSUFFICIENT_UV
SUFFICIENT_UV
Do:
buzz_on = true;
analogWrite(buzz_pin, 127);
rgb_color(255, 0, 1); // Red
delay(100);
rgb_color(0, 0, 0); // Blank
Do:
buzz_on = true

## Slide 13
time_since_last_buzz >= 100
button_state = HIGH
INSUFFICIENT_UV
SUFFICIENT_UV
Do:
buzz_on = true;
analogWrite(buzz_pin, 127);
rgb_color(255, 0, 1); // Red
delay(100);
rgb_color(0, 0, 0); // Blank
Do:
buzz_on = false
analogWrite(buzz_pin, 0);
time_since_last_buzz = 0;
display_seg_and_rgb(uv_index);

## Slide 14
Separate software tests for each component.
Useful for debugging and cascading software for overall program.

## Slide 15
Overall program created from component testing
Updates UV Index every minute
Calculations will alert user for sunblock application.

## Slide 16: Software demonstration components

## Slide 17: Software demonstration overall program

## Slide 18: How well does our design work?
Holding all components
Alternative power supply options (computer through Arduino, 9V battery)
Audible alert (transducer)
Information display (visual 7-seg display and RGB LED)

## Slide 19: reflections
Successfully achieves key requirements and specifications
Future improvements include:
Attachments for various applications
  Ski helmets, bikes, and other outdoor physical exercises.
Product Development
  Microcontroller choices for cost that is better utilized
  Developing consistency of voltage from panel and looking into battery storage
  Looking for more cost-effective solar solutions
Notes: 3 main requirements
To educate users about UV Index in New Zealand
To alert users when outside to reapply sun block, or find shade
To utilise the energy from the sun when outside

## Slide 20
Questions?